## Slide 1
Predicting Motor Failure
24 Hours in Advance
Project Overheat: Predictive Maintenance AI
AeroLogistics, Data Science Division
Shyam Kumar Soni, Data Science Intern
Notes: Introduce yourself and the project: an ML model that warns maintenance teams about motor failures a full day ahead.

## Slide 2
The Problem: Failures Are Costly and Unplanned
Warehouse sorting robots suffer sudden motor failures. Maintenance is reactive, so every breakdown halts operations. The goal: move to proactive maintenance by flagging a failure 24 hours before it happens.
$50,000
lost per minute of downtime
10,000
hourly IoT readings
15
failures (0.15% of data)
24 hours
target warning lead time
Sensors tracked: Temperature, Vibration, Voltage | Period: Jan 2023 to Feb 2024
Notes: Stress the business cost and the extreme class imbalance: only 15 failures in 10,000 hours.

## Slide 3
Approach: Four Phases, Each Avoiding a Common Trap
1
Rolling features
12-hour rolling mean and std of sensor readings capture sustained degradation, not one-off spikes.
2
Target shifting
Failure label shifted back 24 hours so the model predicts the future, not the present.
3
Chronological split
First 80% of time to train, last 20% to test. No shuffling, so no future data leaks into training.
4
Imbalance-aware model
Random Forest (300 trees) with balanced class weights; alert threshold tuned with time-series cross-validation.
Notes: Walk through each phase and the pitfall it avoids: windowing, lead-time, time leakage, class imbalance.

## Slide 4
Results: 2 of 3 Failures Caught in Unseen Future Data
67%
recall: failures caught (2 of 3)
6
false alarms in ~1,990 normal hours
25%
precision on failure alerts
Confusion matrix (test set)
 | Pred. Normal | Pred. Failure
Actual Normal | 1,984 | 6
Actual Failure | 1 | 2
Threshold tuned on training folds only (0.26), not on the test set. The default 0.5 cut-off would have caught just 1 of 3 failures.
Trade-off: a few extra inspections cost far less than one missed failure at $50k per minute.
Notes: Test set had only 3 failures, so results are indicative. Recall was prioritised (F2 score) because a miss is far more expensive than a false alarm.

## Slide 5
Explainability: Vibration Is the Leading Indicator
Chart: Importance by sensor (%)
| Voltage | Temperature | Vibration
Importance | 4.9 | 32.1 | 63
Chart: Engineered 12h features (%)
| Temp Rolling Std | Voltage Rolling Std | Voltage Rolling Mean | Vibration Rolling Std | Temp Rolling Mean | Vibration Rolling Mean
Importance | 1.2 | 1.3 | 1.8 | 3.8 | 15.1 | 21.1
Notes: Mechanics need proof before replacing a $10,000 motor. Feature importance shows sustained vibration, then sustained heating, drive predictions; voltage is a weak signal.

## Slide 6
Recommendation for Maintenance Teams
Monitor vibration
12-hour rolling mean of vibration is the strongest signal (about 21% importance).
Watch temperature
12-hour rolling mean of temperature is second (about 15%). Voltage is weak, so do not base decisions on it.
Act on combined trend
If both 12-hour averages keep climbing together, inspect or schedule a motor swap in the next off-peak window.
Deploy first as a decision-support alert alongside mechanic inspection, not as an automatic replacement trigger.
Notes: Final status in the notebook: ready for deployment as decision support.

## Slide 7
Limitations and Next Steps
Limitations
Only 15 failures overall; just 3 in the test window, so metrics are indicative
Precision is low (25%), giving some false alarms
Single train/test split on one time period
Next Steps
Collect more failure history and retrain regularly
Compare other models (e.g. gradient boosting) and window lengths
Pilot as a live alert system with mechanic review
Thank you
Notes: Be upfront about the small number of failures; it shows sound judgement.